## Slide 2
Thank you for attending NIWeek 2017.
Notes: As a speaker of NIWeek, begin your session by welcoming attendees.
Convey these points:
Your time is valuable, thank you for being at NIWeek 2017.
We aim to make this as valuable as possible, from sharing best practices to helping connect you to fellow engineers and NI experts.

## Slide 4
Notes: Update the color palette to map the old template
Check text box

## Slide 5
A software-centric platform that accelerates the development and increases the productivity of test, measurement, and control systems.
Notes: Our approach is to accelerate productivity, innovation, and discovery through a software-centric platform for developing any system that needs test, measurement, and control.
When spending time and energy making technology work gets in the way of focusing on a solution, we know that’s a big problem. So, our goal is to enable engineers to get their job done faster regardless of their application or industry.

## Slide 6: Tim Vargo
Sandia National Laboratories
Instrumentation Engineer
tdvargo@sandia.gov
Binary Palette
Owner
ravi@binarypalette.com
Ravi Beniwal

## Slide 8: Tried & True, Conventional Debugging Tools
… which still work very well, but with limitations
Built-in Debug Tool | Pros | Cons
Execution Highlighting | Visualizes data flow | Slows execution speed (impedes discovery of timing problems)
Single Stepping | One operation at a time | Slows execution speed (impedes discovery of timing problems)
Breakpoints | Pause execution at this exact point (useful for beginning execution highlighting and single stepping) | Persistent (must remember to remove them before deployment)
Notes: Persistence is both a Pro and a Con

## Slide 9: Tried & True, Conventional Debugging Tools
… which still work very well, but with limitations
Built-in Debug Tool | Pros | Cons
Default Probes | Peek at wire values throughout execution | Difficult to place in clones, Non-persistent
Conditional Probes | + “pause if value” logic | Not available for all datatypes
Custom Probes | + custom view and/or actions | Per LV version
Notes: Probes are commonly called "Watchpoints" in other languages
Conditional Probes are commonly called "Watch Variables" in other languages
Persistence is both a Pro and a Con

## Slide 10: Probes !!!
Review of Generic Probes
  Retain Wire Values
Custom Probes
  Custom Probes Controls (look Mom, no code!)
  Custom Probes NI (native)
    Conditional
  Custom Probes Saphir (3rd party, ViBox – Probes)
  Custom Probes New (roll your own)
  Variant Probe (by Ton Plomp)
Notes: Retain Wire Values keeps wire values in memory so that a probe placed AFTER running the VI can still view the value!

## Slide 11: Often forgotten, overlooked, or just plain ol’ “huh, I-never-knew-about-that”
Suspend when called
  Access this from “SubVI Node Setup”
  Suspends a subVI when called and waits for user interaction
    Allows changes to input values, then re-execute
    Allows changing the output, then return to caller
  A poor-man’s (yet extremely effective) unit testing
  Video Demo: https://youtu.be/AgXcyf2Ta_A

## Slide 12: There are many Free, 3rd-party Debugging Tools These two will retain information even if LabVIEW crashes!
WinDebugLogging
  Write debug strings to the Windows debug interface
  Dr. Damien (DFGray), Nov-2008
  DebugView (from Sysinternals [Microsoft])
WinDebugLogProbe
  Tim Vargo
Notes: Using the Windows debug interface retains information even if LabVIEW crashes!

## Slide 13: NI debugging tools
Event Inspector
  Introduced with LabVIEW 2013, the Event Inspector added an ability to gain new understandings into the inner workings of our event structures
Built-in to LabVIEW

## Slide 14: NI debugging tools
VI Analyzer
  VI Analyzer does its job well, but it intends to perform a static analysis of VIs, not a dynamic analysis of code while running
Toolkits for extra cost (but worth it)

## Slide 15: NI debugging tools
Desktop Execution Trace Toolkit (DETT)
  The DETT product is very good at what it was designed to do
    dynamic execution traces provide a fantastic wealth of evidence when event timing and/or sequence information is critical
    … but they don’t provide non-event related information
Toolkits for extra cost (but worth it)

## Slide 16: Some impediments to advanced troubleshooting …
All of these built-in tools are extremely useful during troubleshooting of individual VIs or small collections of Vis
  particularly when we already know which VIs are the troublesome ones
  but the LabVIEW IDE still lacks a debugging tool to provide insights with a "bigger picture" view of an entire project
Using only the native troubleshooting tools
  reentrant VIs are especially difficult to debug, since each preallocated clone will have its own data space in memory
  shared clones are even more complex since they share data space
Dynamically launched VIs, even if not reentrant, present their own particular frustrations during a debug session, since the developer is unable to place probes BEFORE executing the code.

## Slide 17: As LabVIEW enthusiasts, we all love visuals
… but THESE visuals make our faces cringe, and our sphincters tighten
WHAT?! There are still VIs running?!

## Slide 18: What to do when debugging becomes too complex ???
How to defeat these shortcomings, and many other debugging related challenges …
  have long been the topics of many user community discussions
  several ad-hoc solutions and processes, although usually quite limited in scope, have been developed over the years by the user community
  but they lack the coherence of a unified tool
Introducing the

## Slide 19: LabVIEW Task Manager
Providing a dynamic & big-picture view of all VIs currently in memory
Conquering those difficulties concerning reentrancy, clones, dynamic launching, finding & aborting hung VIs, and other sticky complications
By delivering new comprehensions into your running code
By enabling interaction with individual or groups of VIs in many various ways, providing significant benefits while troubleshooting
The LabVIEW Task Manager seeks to be that missing unified debugging tool

## Slide 20: Application Instance
The LabVIEW Task Manager (LVTM) detects all open LabVIEW application instances, but discovers and displays VIs for only the selected instance

## Slide 21: Menu: View
The View menu provides options to set an update speed for refreshing the view and a few view options

## Slide 22: Menu: View>>Group By Library
Group By Library displays all VIs in the selected application instance grouped by the library they belong to. All VIs that are not part of any library are shown under <no parent library>.

## Slide 23: Menu: View>>Group By Folder
Group By Folder displays all VIs in the selected application instance with their folder hierarchy on disk. This view makes it easy to see where all the project dependencies live on disk.
Notes: It is in this view where items can be excluded from being displayed, which we will see in a few slides later.

## Slide 24: Menu: View>>Flat List
Flat List displays all VIs in the selected application instance as a list. This view can help sorting the view by different properties of the VIs, by clicking on the column headers.
Notes: In particular, sorting the flat list view by State will help distinguish between Idle, Running, and RunTop (top-level) VIs; which can be very useful when looking for VIs that are still running that you thought should not be. VIs with a State of RunTop can then be aborted!

## Slide 25: Menu: Filters
The Filters menu items provides several settings for filtering out items from view. Once all items in memory, for the selected application instance, are displayed in the tree, certain dynamic properties of all VIs (such as State, Paused status, Execution Highlight status, Data size, etc.) are occasionally checked and updated. The more VIs that need to be checked, the more resources are tied up, and the longer each update cycle takes.
Filtering out VIs that you don’t currently care about can tremendously improve performance of the LVTM. Select (√) the filter options that you want to apply, and all VIs that match these filters will be ignored.

## Slide 26: Menu: Filters>>Extensions
Select (√) the file extensions that you want to filter out of the view. All files with the selected extensions will be ignored.

## Slide 27: Menu: Filters>>Types
Select (√) the VI types that you want to filter out of the view. All VIs of the selected type will be ignored.

## Slide 28: Shortcut Menu: Filter Out …
While in the Group By Folder view, right click any folder and select Filter Out This Folder, adding that folder to an exclusion list. Or you can select Filter Out All But This Folder, which will add all remaining folders to the exclusion list. Any VIs in these filtered out folders will no longer show up in the tree.
Although filtered paths can only be added or removed while in the Group By Folder view, the hidden paths will persist in other views. This helps the user to de-clutter the view, and can also greatly improve performance.

## Slide 29: Menu: Filters>>Paths
If one or more paths have been filtered out, they will show up under the Filters>>Paths menu. Clicking any of these paths will remove it from the exclusion list, and the view will be immediately updated.
Selecting Remove All will remove all filtered out paths, effectively disabling path based filtering.

## Slide 30: Progress Update
Any time changes are made to the filters or to the view, the view is refreshed. Discovering all VIs in memory, along with their clones, and then updating the tree view, can take several seconds. A progress bar at the bottom right of the screen, in the status bar, shows the discovery and update progress.

## Slide 31: Toolbar
LVTM provides several operations that can be performed on one or more selected VIs in the tree. These operations may be invoked from the toolbar buttons at the bottom of the screen.
These same operations may also be invoked from the right click shortcut menu.
Open Front Panel(s)
Close Front Panel(s)
Open Block Diagram(s)
Close Block Diagram(s)
Highlight Execution(s)
Do Not Highlight Execution(s)
Pause Execution(s)
Resume Execution(s)
Toggle Execution(s)
Abort VI(s)

## Slide 32
And now for the
DEMO
!!!!!!!!!!!!!!!!!!!!!!!

## Slide 39
QUESTIONS?

## Slide 40
We must avoid “drawing vast conclusions from half-vast data”
— Jerry R. Ehman, SETI Astronomer

## Slide 41
Notes: We want your feedback. Please take one minute to complete the session survey.

## Slide 42: LabVIEW Task Manager

## Slide 43
Notes: Convey these points:
Thank you for attending NIWeek 2017.
There’s many ways to stay connected.
You can download the session materials through the mobile app or at ni.com/niweekcommunity.
If you’re interested, you can reach me at [share your email]